## Slide 1: Improving Continuous Glucose Monitoring with Smoothing Filters
[Robin Ouzts]
11/31/2017

## Slide 2: Overview
Background
  Continuous Glucose Monitoring
  Study Motivation
  Smoothing Filters
Methodology
  Data Uploading / Retrieval
  Parsing and Analysis
Results
  Plots
Conclusion and Summary
References

## Slide 3: Background

## Slide 4: Continuous Glucose Monitoring
Inserted subcutaneously
Lag time of 5-15 min between interstitial fluid and blood glucose [2]
Glucose + GOx − FAD+ → Glucolactone + GOx − FADH2
GOx − FADH2 + O2 → GOx − FAD + H2 O2
H2O2 → 2H+ + O2 + 2e
Platinum anode measures electron transfer from oxidized H202 proportionally to glucose present [3]
Image from [1]

## Slide 5: Continuous Glucose Monitoring
A CGM provides real-time, frequently updated blood glucose estimates without the need for a finger prick.
The most popular CGMs on the market are made by Dexcom (G4, G5) and Medtronic (Enlite).
Requires calibration to remove variance from sensor depth, location, etc.
Dexcom smooths their data to remove noisy outliers, and is conservative with displayed data
  No data during calibration period (2 hours)
  Single bad point can result in no data for hours
Continuous Glucose Monitoring cont.
Image from [4] (top) and [5] (bottom)

## Slide 6: Continuous Glucose Monitoring
Nightscout
  Developed by parents of children with T1D
  Uploads Dexcom data to the Cloud
  Allows for access to data that Dexcom hides (e.g. unfiltered data and calibration details)
  Allows for solutions to several issues with using the Dexcom device by itself
Dexcom and Nightscout
*Images on this chart and the following 4 taken from [6]

## Slide 7: Dexcom is Conservative

## Slide 8: Single Bad Data Point Causes Loss of Data

## Slide 9: Dexcom Doesn’t Deal With Heavy Noise

## Slide 10: No Data During Restart Period

## Slide 11: However…
Some filtering is good
  Raw data can be too noisy at times
  Ideally, we would be able to see the filtered data even when it may be suspect (heavy noise, calibration period, etc.)
  Dexcom probably hides this to avoid liability and the exact details of Dexcom’s filter are proprietary
How can we best approximate the Dexcom G4’s data smoothing filter?

## Slide 12: Smoothing Filters
We will examine four methods of smoothing:
  Savitzky-Golay
  Least Squares Fit
  Moving Average
  Hamming Window Function
We don’t expect to outperform the Dexcom algorithm – we just want to come reasonably close
Filtering is a very complex and broad subject that many people have dedicated their lives to. Explaining these filters in depth is far beyond the scope of this talk, and I am far from an expert regardless!

## Slide 13: Savitzky-Golay in 30 Seconds
Digital filter designed by Abraham Savitzky and Marcel Golay [7]
  Considered one of the 10 Seminal Papers ever published in Analystical Chemistry
Moves along the curve in a window of data points
Fits a local polynomial to the curve
Red/Yellow Line in the animation shows the local polynomial being fitted
Circles are smoothed values
Graphic taken from [9]

## Slide 14: Least Squares Fit in 30 Seconds
Whereas Savitzky-Golay fits a polynomial to many sub curves, here we try to fit a single polynomial to the entire curve.
In retrospect, this is a poor choice, because the data is so noisy and jagged that it is not well approximated this way, especially by low degree polynomials.
This algorithm attempts to minimize the sum of squared differences between the data and a fit.
Graphic taken from [10]

## Slide 15: Moving Average (Flat) in 30 Seconds
This is a simple but often effective means of smoothing
  Often used in technical analysis of stocks [8]
Look at the data in windows of size w and average it over that period
As with the other filters, the choice of the window size is critical
  If w=1, we are averaging only a single point and we produce the exact same curve!
  If w is large, we create a curve that is “too smooth” and loses too much detail.
  Ultimately, choice of window size is determined by your specific needs – there is no “best” size.

## Slide 16: Hamming Window in 30 Seconds
The Hamming Window is widely used in signal processing [6]
May not directly apply to BG readings
In signal processing, it is used to minimize the height of the highest sidelobe
Similar to a cosine wave
Graphic taken from [11]

## Slide 17: Methodology

## Slide 18: Continuous Glucose Monitoring
Nightscout Site Created
  https://robinsbloodsugar.herokuapp.com
  Followed the instructions to create a Nightscout site and used an Android device to upload the data to it
Problem – How to export the data?
  Nightscout (seemingly) does not provide an easy way to export the data from the site – it is visual only
  As part of the set up process for Nightscout, a MongoDB database was created.
  Some googling led to the following 3-line R script (details redacted) shown below to retrieve the data in JSON (JavaScript Object Notation, similar in form to a Python dictionary) format
Step 1 – Getting the Data
require(mongolite)
con <- mongo(collection="entries",url="mongodb://USERNAME:PASSWORD@DBURL",db = “DBNAME")
con$export(file("dump.json"))

## Slide 19: Continuous Glucose Monitoring
Python’s built in JSON parser makes parsing the output simple
One issue – the raw data shown on the Nightscout site isn’t present in the data. Instead, calibration details (in milliamps!) are used.
  Scoured the Nightscout source code on GitHub for the formula they use to calculate the raw data from this and copied it:
Apply the Filters
  SciPy has built in implementation for Savitzky-Golay filtering
  Examples for various windowing functions also present in SciPy cookbook – adapted these for Flat and Hamming filtering
  Least squares fit done by creating a polynomial using numpy.polyfit and evaluating it using numpy.poly1d
Step 2 – Parse and Filter the Data

## Slide 20
Question: How do we evaluate the results?
  Many metrics could be used.
  I used the average deviation from the Dexcom filter data
  Thus, the “best” filter is the one that is, on average, most similar to the Dexcom filter data.
Other metrics could be of interest
  Minimum/maximum displayed blood glucose
  Average standard deviation
  Etc. (I use R’s summary function to calculate a variety of descriptive statistics)
Step 3 – Concluding Something

## Slide 21: Results

## Slide 22
Filter Output

## Slide 23
Savitzky-Golay

## Slide 24
Least Squares

## Slide 25
Moving Average / Flat

## Slide 26
Hamming

## Slide 27
Results
The differences between all of the curves except for Least Squares is quite subtle
However, the Savitzky Golay filter was the closest match to the Dexcom data by our minimum mean metric.
However, note that it also produced the largest extrema – both max and minimum – even compared to the Dexcom data. The low of 34.57 could be especially misleading!
Note – again – that window sizes and polynomial orders could significantly impact this analysis.
> df <- read.csv('PlotData.csv')
> summary(df$SGV)
Min. 1st Qu. Median Mean 3rd Qu. Max.
43 109 146 150 186 354
> summary(df$Raw)
Min. 1st Qu. Median Mean 3rd Qu. Max.
39.57 108.28 146.28 151.14 188.27 360.09
> summary(df$SavitzkyGolay)
Min. 1st Qu. Median Mean 3rd Qu. Max.
34.57 108.16 146.53 151.14 188.31 360.62
> summary(df$LeastSquares)
Min. 1st Qu. Median Mean 3rd Qu. Max.
88.91 143.97 153.45 151.39 160.28 177.84
> summary(df$Flat)
Min. 1st Qu. Median Mean 3rd Qu. Max.
43.38 109.59 147.03 151.15 187.28 348.78
> summary(df$Hamming)
Min. 1st Qu. Median Mean 3rd Qu. Max.
42.59 108.83 146.27 151.15 188.17 355.44

## Slide 28: Summary and Conclusion

## Slide 29
Summary
Four smoothing methods were compared against the Dexcom G4’s smoothed data using real blood glucose data derived from a CGM.
Python (using NumPy, SciPy, and Matplotlib) in addition to R were used to analyze the data.
The Savitzky-Golay filter produced the closest match to Dexcom’s smoothed data, but also produced worse extrema than any other method.
This approach could be used to fill in gaps in data when the Dexcom does not output a data point due to noisy data or a calibration period.

## Slide 30: References

## Slide 31
References
1. Continuous Glucose Monitoring System. (2013, Feb 25). Retrieved December 01, 2017, from http://www.apiindia.org/medicine_update_2013/chap43.pdf
2. Sato,J.; Hirose, T.; Watada, H. (2012, Feb). “Continuous glucose monitoring system: Is it really accurate, safe and clinically useful?.” Journal of Diabetes Investigation. 3(3): 225-230.
3. Yoo, E.; Lee,S. (2010). “Glucose Biosensors: An Overview of Use in Clinical Practice”. Sensors(Basel). 10(5): 4558-4576. doi:10.3390/s100504558.
4. Russell, S. J., MD. (2017, June). Continuous Glucose Monitoring. Retrieved November 30, 2017, from https://www.niddk.nih.gov/health-information/diabetes/overview/managing-diabetes/continuous-glucose-monitoring
5. Dexcom. (n.d.). Retrieved November 30, 2017, from https://cdn2.asweetlife.org/wp-content/uploads/2013/10/Dexcom-CGM-Dexcom-G4-Platinum.jpg
6. Interpreting Raw Dexcom Data. (2015, February 13). Retrieved November 30, 2017, from http://www.nightscout.info/wiki/labs/interpreting-raw-dexcom-data
7. Savitzky, A.; Golay, M.J.E. (1964). "Smoothing and Differentiation of Data by Simplified Least Squares Procedures". Analytical Chemistry. 36 (8): 1627–39. doi:10.1021/ac60214a047.
8. Devcic, J. (n.d.). Weighted Moving Averages: The Basics. Retrieved November 30, 2017, from https://www.investopedia.com/articles/technical/060401.asp
9. Savitzky-Golay filter. (2013, January 29). Retrieved November 30, 2017, from https://en.wikipedia.org/wiki/Side_lobe#/media/File:Typical_Antenna_Pattern.jpg
10. Linear least squares. (2011, June 9). Retrieved November 30, 2017, from https://en.wikipedia.org/wiki/Linear_least_squares_(mathematics)#/media/File:Linear_least_squares_example2.svg
11. Side lobe. (2007, April 6). Retrieved November 30, 2017, from https://en.wikipedia.org/wiki/Side_lobe#/media/File:Typical_Antenna_Pattern.jpg